## Slide 1: Project: QB50 Ground data architecture - options
Muriel Richard
CEM Meeting
3 December 2012

## Slide 2: Expected types of data
QB50 Science Unit data
  Science data generated by the Science Unit (TBD – MSSL)
  HK generated by the Science Unit
QB50 Science related Housekeeping data (Sc-HK): what is needed to process the science instrument data
  Time tagged setting parameters of the science instruments (TBD – MSSL)
  Time tagged attitude sensors (sun sensors, gyros…)? (TBD – Surrey)
  Time tagged quaternions? (TBD – Surrey)
  Time tagged temperature sensors?
  Other…?
CubeSat HK data
  All data relative to the health of the CubeSat, not needed for science purposes

## Slide 3: RA requirements (G. Shirville)
Amateur radio communications have to be “open” (Article 25.2A of the Radio Amateur Regulations that have been agreed by all member states of the ITU).
Normally this presents no problem to cubesat operators in regards to housekeeping data but the same obligation also applies to all science data as well. There can be no copyright or IPR on data downlinked from a spacecraft using the amateur satellite service.
Command uplinks can be encrypted but nothing else can be.
The RA service is intended as a “one to many” system so all amateurs should be allowed to receive and decode all transmissions. If the encoding method is not a recognised standard already in use within the amateur fraternity then the developers should make the ground segment software available for free download before launch.

## Slide 4
AX.25 FRAME
X
Packet
X
Packet
...
RF Modulation X
AX.25 FRAME
X
Packet
X
Packet
...
X
Packet
AX.25
Modulated
frames
At GS:
Demodulation (De-mod)
AX.25 frames
“De-framing” software (De-fram)
“De-packetizing” software (De-pack)
(done in MCS/Satellite
Control Software - SCS)
X packets
DATA: HK, raw science data, etc… located in SCS Database
Downlink data
processing

## Slide 5: Protocols
AX-25 frames
SwissCube tailored ECSS-PUS - packets
Telemetry

## Slide 6: Architecture 1
VKI Server
DPAC at BUSOC
De-mod X
De-fram X
De-pack X
Sat Control X
De-fram A
De-pack A
De-fram X
De-pack X
De-fram X
De-pack X
De-mod X
De-fram A
De-pack A
De-mod X
De-fram B
De-pack B
De-fram C
De-pack C
De-fram D
De-pack D
De-fram E…
De-pack E…

## Slide 7: Architecture 2 (S3)
VKI Server
DPAC at BUSOC
De-mod X
De-fram X
De-pack X
Sat Control X
De-mod X
De-mod X

## Slide 8: Architecture 3:
Insert a specific header field in AX.25 that specifies if data is QB50 science or not
  Frames that are QB50 would be sent directly to VKI server
  All frames/packets sent anyway to CubeSat teams
  Need to check implications of this changes to AX.25 protocol (current SW will not comply with it)
Need for a pre-defined QB50 packet format that is imposed on all teams
  Packet format could follow ECSS-PUS - Science Service
  CubeSat teams will need to code themselves this format on-board their OBC/COM
Each CubeSat team in charge of the implementation of the CubeSat data decoding (at GS, or servers?)
Insert QB50 field?

## Slide 9: Architecture 3
VKI Server
DPAC at BUSOC
De-mod X
De-pack X
Sat Control X
De-mod X
De-mod X
De-fram Modified AX.25
De-pack X,Y
De-pack QB50
De-pack QB50
De-fram Modified AX.25
De-fram Modified AX.25
De-pack A,B,C,D….
De-pack QB50
De-fram Modified
AX.25
De-pack X,Y
De-pack QB50

## Slide 10: Conclusions
Define the science and HK data format and provide it to team
  Proposal: EPFL can propose the ECSS-Payload service format
  Need to check that this solution fits needs
Discuss with GFWG, GENSO, VKI, BIRA and others to define where packet data processing is done
Most of these questions can be resolved with meeting of the right people, hopefully during January’s meeting of the GFWG