## Slide 1: Space Weather in situ measurements perspective
Andrew Fazakerley
Mullard Space Science Laboratory (UCL)
UKSP Solar Missions Forum 09 Feb 2017

## Slide 2: L5/L1 Space Weather Warning System
Interplanetary Coronal Mass Ejections (ICMEs)
Earth
L5
Sun
L1
Hazard Potential
sudden magnetospheric compression - GICs
possible prolonged Bz -ve, geomagnetic storm
radiation belt enhancements, SEPs (sheath)
Forecasting needs measurements at
L5 RS: active regions (caution)
L5 RS: Earthward ICME (clear risk)
L1 RS : coronagraph (>~ 1 day halo CME alert)
L1 IS : n, V, B (~ 1h geoeffectivity alert)

## Slide 3: L5/L1 Space Weather Warning System
Earth
L5
Sun
L1
Stream Interaction Regions (SIR) and High Speed Streams (HSS)
Hazard Potential
Radiation belt enhancement from fast streams
sudden compression of magnetosphere - GICs
Forecasting needs measurements at
L5 RS: near-equatorial coronal holes (caution)
L5 IS: measure fast streams, waves (caution)
L1 IS : n, V, B (~ 1h geoeffectivity alert)

## Slide 4: L5/L1 missions: In situ measurements (UK focus)
Magnetometer (Imperial College)
Solar Wind Analyser (MSSL/UCL)
Double Star FGM: Carr et al 2005
Solar Wind Analyser concept, developed from Solar Orbiter SWA-EAS
Preliminary study sets out requirements and shows importance of minimising spacecraft magnetic field, and using a long boom
Emphasis on reliability and longevity
Preliminary study sets out requirements and shows how a development of SWA-EAS can deliver the requirements.
Emphasis on reliability and longevity

## Slide 5: Earth-orbiting missions: In situ measurements (UK focus)
QB50 (MSSL/UCL)
HOPE-M (MSSL/UCL)
HOPE-M, breadboard
novel mini- analyser design
Fleet of cubesats to launch in 2017 to study lower thermosphere.
Several types of small sensor, (INMS, FIPEX, LP)
INMS x 14 from MSSL, novel mini-analyser design
ESA funded breadboard
Small sensor for GEO satellites
Measure plasmas causing spacecraft charging that causes anomalies
“SWAN” design variant, optimised for solar wind, was planned for Sunjammer mission

## Slide 6: Also…
Current
  DSCOVR now operating at L1,
  measuring solar wind
  Proba-2: 2 year extension recently approved (includes SWAP solar disk imager)
Future
  SMILE – ESA-CSA small mission, SpW theme, will be first to image boundaries of magnetosphere, in soft X-ray, also image aurora
  (THOR late 2020s if selected)